## Slide 1
What each part of March MSS catches
M0 ⇕
w0
M1 ⇑
r0
r0
w1
w1
M2 ⇑
r1
r1
w0
w0
M3 ⇓
r0
r0
w1
w1
M4 ⇓
r1
r1
w0
w0
M5 ⇕
r0
Part of the test
Faults it targets
Injected in our simulation
M0 ⇕(w0)
Puts every cell in a known state; detects nothing on its own.
—
1st read (r0 / r1)
Stuck-at (SAF), transition faults (TF) left by the previous write, read-destructive (RDF) and incorrect-read (IRF) faults.
SAF0, SAF1 (Croc, --mbist-fault); RDF (tb_march_bist_top)
2nd read (r0 / r1)
Deceptive read-destructive (DRDF): the 1st read returns the right value but flips the cell, so only the 2nd read sees it.
Not injected (DRDF mask exists, unused)
1st write (w1 / w0)
Transition write (0→1 or 1→0): sensitises up and down transition faults, caught by the next read.
TF 0→1 (tb_march_bist_top)
2nd write (w1 / w0)
Non-transition write (same value again): sensitises write-destructive faults (WDF), caught by the next read.
Not injected (WDF mask exists, unused)
⇑ then ⇓ order
Two-cell coupling faults with the aggressor below (⇑) or above (⇓) the victim: CFst, CFds, CFtr, CFwd, CFrd, CFdrd, CFir.
Not injected (CF masks exist, unused)
M5 ⇕(r0)
Final read: catches faults sensitised by the last w0 of M4.
—
Caveats: our controller writes solid all-0 / all-1 words, so coupling between bits of the same word is not fully covered. The coverage claim comes from the paper; only the green faults were injected in simulation.
March MSS (18N) covers all unlinked static faults in RAMs. Algorithm by G. Harutyunyan, V. A. Vardanian and Y. Zorian,
“Minimal March Tests for Unlinked Static Faults in Random Access Memories”, Proc. IEEE VLSI Test Symposium (VTS), 2005.
Notes: 8 clicks: one table row per click (the matching operations light up in the element bar), then the caveats. Algorithm credit: G. Harutyunyan, V. A. Vardanian, Y. Zorian, 'Minimal March Tests for Unlinked Static Faults in Random Access Memories', IEEE VTS 2005. In our RTL the fault model (RM_IHPSG13_1P_core_behavioral_bm_bist_fault_model.v) supports SAF, TF, RDF, IRF, DRDF, WDF and coupling masks; Croc's --mbist-fault run enables SAF0/SAF1 and tb_march_bist_top enables SAF1, TF 0->1 and RDF.

## Slide 2
March MSS (18N) MBIST on an 8-word SRAM
M0 ⇕
w0
M1 ⇑
r0
r0
w1
w1
M2 ⇑
r1
r1
w0
w0
M3 ⇓
r0
r0
w1
w1
M4 ⇓
r1
r1
w0
w0
M5 ⇕
r0
SRAM (word = 8 bits)
addr 0
10010010
addr 1
00100100
addr 2
01001001
addr 3
10010010
addr 4
00100100
addr 5
00000000
addr 6
10010010
addr 7
00100100
SAF0
Before the run
Word 5 has a stuck-at-0 fault: writing 1 has no effect.
The controller runs on TCK and is started from SoC Regs (MBIST START) or JTAG.
Each read compares the whole word with all-0 or all-1.
Error-address FIFO (4 deep)
busy
0
done_o
0
fail_o
0
8-word SRAM, 6 March elements, 18 operations per word (144 in total).
Click to start the test.
Element M0
⇕(w0)
Write 0 to every word to initialise.
addresses 0 → 7
M0 ⇕(w0): initialise the whole SRAM to 0.
busy
1
00000000
w0
00000000
w0
00000000
w0
00000000
w0
00000000
w0
w0
00000000
w0
00000000
w0
✓
Element M1
⇑(r0,r0,w1,w1)
Going up: read 0 twice, then write 1 twice.
addresses 0 → 7
M1 ⇑(r0,r0,w1,w1): double reads catch read-destructive faults,
double writes catch write-disturb faults.
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
r0 r0 ✓ w1 w1 lost
Write lost
addr 5 op w1
write 11111111
stored 00000000
Nothing flags it yet: only a later read can catch it.
Word 5 is stuck at 0, so the write of 1 is silently lost.
The reads of 0 before it still pass.
Element M1
⇑(r0,r0,w1,w1)
Going up: read 0 twice, then write 1 twice.
addresses 0 → 7
M1 ⇑(r0,r0,w1,w1): double reads catch read-destructive faults,
double writes catch write-disturb faults.
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
✓
Element M2
⇑(r1,r1,w0,w0)
Going up: read 1 twice, then write 0 twice.
addresses 0 → 7
M2 ⇑(r1,r1,w0,w0): every word should now read all 1s.
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
r1 r1 ✗ w0 w0
MISMATCH
addr 5 op r1
read 00000000
expected 11111111
The fault is detected in M2.
Read of word 5 returns 0 where 1 is expected: fault detected.
addr 5 (M2)
fail_o
1
Address 5 is pushed into the error FIFO and fail_o goes high. The second r1 fails too,
but each address is logged only once per element (read_logged).
Element M2
⇑(r1,r1,w0,w0)
Going up: read 1 twice, then write 0 twice.
addresses 0 → 7
M2 ⇑(r1,r1,w0,w0): every word should now read all 1s.
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
✗
Element M3
⇓(r0,r0,w1,w1)
Same as M1, going down.
addresses 7 → 0
M3 ⇓(r0,r0,w1,w1): repeating the test going down catches coupling faults
between neighbouring cells.
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
r0 r0 ✓ w1 w1 lost
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
11111111
r0 r0 ✓ w1 w1
✓
Element M4
⇓(r1,r1,w0,w0)
Same as M2, going down.
addresses 7 → 0
M4 ⇓(r1,r1,w0,w0): second check for all 1s, going down.
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
r1 r1 ✗ w0 w0
MISMATCH
addr 5 op r1
read 00000000
expected 11111111
Detected again, now going down.
addr 5 (M4)
Same fault, found again in M4: address 5 gets a second FIFO entry.
Element M4
⇓(r1,r1,w0,w0)
Same as M2, going down.
addresses 7 → 0
M4 ⇓(r1,r1,w0,w0): second check for all 1s, going down.
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
00000000
r1 r1 ✓ w0 w0
✗
Element M5
⇕(r0)
Final read: every word must hold 0.
addresses 0 → 7
M5 ⇕(r0): final read, every word must hold 0.
r0 ✓
r0 ✓
r0 ✓
r0 ✓
r0 ✓
r0 ✓
r0 ✓
r0 ✓
✓
busy
0
done_o
1
Run complete
144 operations = 18N
FIFO holds addr 5 twice (M2 and M4).
A fault-free SRAM ends with an empty FIFO and fail_o = 0.
Software (or JTAG) reads STATUS, then pops the FIFO through the ERRADDR registers
in SoC Regs to get the failing addresses. A full FIFO stops the run (ERR_ABORT).
Notes: 14 clicks. Sweeps play by themselves after a click; the run pauses at the fault so you can explain it. March MSS: {⇕(w0); ⇑(r0,r0,w1,w1); ⇑(r1,r1,w0,w0); ⇓(r0,r0,w1,w1); ⇓(r1,r1,w0,w0); ⇕(r0)} = 18N. Word 5 is stuck at 0: the w1 writes are lost, so the r1 reads in M2 and M4 fail. Each failing address is logged once per element in the 4-deep error FIFO and fail_o goes high. Software or JTAG then reads STATUS and pops the FIFO through the ERRADDR registers in SoC Regs. Use Back (left arrow) to step backwards.