## Slide 1
VAD: debug, observability and controllability registers
Before: software could only switch the VAD on, set the thresholds and get yes / no back. Now it can see inside every step and drive it.
Microphone
(I2S)
Frame buffer
2 SRAM banks, ping-pong
DSP core
energy + zero crossings
Decision
vs thresholds
Wake-up
speech / no speech
Software over the bus (register interface)
enable,
thresholds
Before: only this yes / no
came out of the VAD
Frame memory access
Control: pause the microphone, write your own audio frame and run the core on it.
Observe: read back the audio that was really stored.
Controllability
Observability
Last frame result + evaluate
Observe: see the energy and zero-crossing values the core computed, not just yes / no.
Control: write your own values and run only the decision, to test the thresholds without audio.
Observability
Controllability
Status + interrupt
Speech flag: held until software clears it, so no detection is missed.
Buffer: which bank fills, which is processed, how full the frame is.
Interrupt: software switches it on, fires it on demand to test it, and clears it.
Observability
Controllability
Same chip, only these registers cut off vs. reachable: test coverage from the pins 17 % → 28 %, DSP core 5 % → 24 %.
One bus access (2 cycles) while the chip runs, instead of stopping it and shifting every flip-flop (~300 shifts).
Notes: Start: the original VAD. Software writes enable and the two thresholds and only gets the wake-up bit back, so a wrong decision cannot be traced to the microphone data, the energy / ZCR computation or the thresholds. Click 1: frame memory access. Software takes the frame SRAMs (audio is dropped meanwhile), writes or reads samples with auto-increment and kicks the core on a chosen bank: a known stimulus in, the stored audio out. Click 2: the core keeps the energy and zero-crossing count of the last frame in registers; software can read them, or write values and run only the comparator (EVAL), which sets the speech flag like a real frame. Click 3: the core's speech output is a one-cycle pulse per frame; the sticky flag holds it until software writes 1 to clear it. Status also shows which ping-pong bank the microphone fills and which the core reads, the next sample slot of the writer (does audio arrive, how full is the frame) and a read-pending bit for SRAM debug reads. Interrupt: before, the line was the raw one-cycle decision pulse, which software could not mask, acknowledge or catch while busy. Now it is the sticky flag AND an enable bit (held until cleared), software can fire it on demand with the IRQ_TRIG command (no audio, works outside debug mode) and read the line back in the status register, so the whole path flag, enable, line, CPU can be tested. Click 4, first line: TetraMAX pins-only ATPG on the same DEMO netlist with the same limits, once as built and once with OBI address bit 6 tied to 0 so these registers are unreachable: 28.3 % vs 17.0 % fault coverage, DSP core 23.5 % vs 5.0 %. Of the 2858 faults only detected with the registers, 1433 were not observed and 792 not controlled without them. Second line: measured in gate-level simulation on the synthesized netlists: an OBI write of a threshold takes 2 cycles; the same through the scan chain needs one full recirculating pass (299 flops in NORMAL, 560 in DEMO) with the clock in test mode, and the SRAM contents are not reachable by scan.