## Slide 1
How the additions were verified
Every feature is checked on its own, then with software on the CPU, then from the chip pins like a tester.
1
Unit
One block with simple models around it
Used for
VAD registers, March BIST with injected memory faults
2
SoC
Real C programs running on the CPU
Used for
Memory BIST, VAD interrupt, original Croc tests
3
Chip pins
Only the pins and JTAG, as on a tester
Used for
Boundary scan, crossbar isolation, sub access
Self-checking
Every check prints pass or fail, and each run ends with a count. Nothing is judged by eye.
Used as in silicon
Each feature is driven the way it will be used: by software over the bus, by a tester over JTAG, or both.
Negative controls
Deliberately broken hardware or wrong expectations must make the test fail, and they do.
Notes: Clicks 1-3: the three levels. Unit: a testbench around one block (tb_vad_sram_dbg, tb_march_bist_top with a behavioural SRAM fault model). SoC: C programs on the CVE2 core in tb_croc_soc (test_mbist, test_vad_mbist, test_vad_irq, the original Croc tests). Chip: tb_croc_chip, only the pads; JTAG drives boundary scan (+bscan_test) and crossbar isolation / sub access (+obi_jtag_test). Click 4: the principles. Negative controls: the VAD testbench was run against the RTL without the new interrupt bits and failed at those checks; test_vad_irq with one wrong expectation reports FAIL with that check's number.

## Slide 2
Verification per feature
Self-checking runs in RTL simulation. Counts are checks passed / checks run.
Feature
Tested at
What the test shows
Result
Boundary scan
Chip pins
Reads and drives every pin, feeds the core from the scan cells, then hands the pins back
34 / 34
March BIST
Unit, SoC, chip
All memories pass from software and JTAG; unit test runs with injected memory faults
SoC + chip pass
Crossbar isolation
Chip pins
Each route and the error path, a remapped address map, nothing leaks while isolated
18 / 18
Subordinate access
Chip pins
JTAG writes and reads a real memory; each transfer arrives exactly once; errors come back
25 / 25
VAD observability
Unit
Frame memory access; energy and zero crossings match a model; decision on chosen values
1,095 / 1,095
VAD interrupt
Unit, SoC
Fired on demand, seen in the VAD and the CPU, taken once, cleared by software
Pass
Testability
ATPG
Same netlist, registers reachable vs. cut off: pin-level fault coverage 17 % → 28 %
+11 points
No regressions
SoC, chip
The original Croc tests still pass with every addition in place
10 / 10
RTL simulation only: no gate-level or tester runs yet. The boundary-scan and isolation runs are older than the
last RTL edits and need a rerun; the BIST fault-injection unit results are still to be added.
Notes: Click 1: the DFT features. Boundary scan: tb_croc_chip +bscan_test, 34 checks (chain lengths for BYPASS / SAMPLE / EXTEST / INTEST, walking patterns, INTEST with the core echoing inputs, release). March BIST: test_mbist and test_vad_mbist pass on tb_croc_soc and tb_croc_chip; the unit test tb_march_bist_top injects stuck-at, transition and read-disturb faults (result to be filled in). Crossbar isolation: tb_croc_chip +obi_jtag_test, 18 checks; with subordinate access 25 checks including the kept JTAG map. Click 2: VAD. tb_vad_sram_dbg, 1095 checks including the interrupt trigger and read-back; test_vad_irq on the SoC checks the VAD status bit, the CPU pending bit and the handler. Click 3: ATPG ablation on the DEMO netlist, 28.3 % vs 17.0 % pins-only fault coverage. Regressions: helloworld, print_config, clint, compute, gpio, obi_timer, soc_ctrl, uart, interrupts on the SoC and helloworld on the chip; test_idma not re-run. Simulators: Questa on 31 Oct; Verilator 5.020 on 1 Nov for the VAD testbench, test_vad_irq and test_interrupts.